Standard Operation Procedure for Imaging Radioactive Animals in the Optical Imaging Lab

Update date: June 3, 2015

_______________________________________________________________

I. Purpose: This SOP provides investigators and BRIC-Small Animal Facility (SAI) staff with general guidelines on conducting imaging procedures on radioactive animals in the optical imaging lab, room SB223.

II. General Procedures:

- Prior to your imaging study, please send email notice to bricsai@med.unc.edu, regarding your radioactive animal imaging study in room SB223, including radioisotope information, number of animals, and study duration.

- If possible, always schedule your imaging study at the end of the day to minimize any potential radiation hazards exposure.

- Prior to imaging in Room SB223, a survey will be conducted using the Geiger counter, and background level will be recorded in the radiation log sheet.

- Absorbent sheets will be needed to cover all the counter top space that has potential animal contact, including space for animal cages and animal procedures.

- Users or staff are required to wear lab coats, goggles, and gloves. A radiation badge is required for RAM workers.

- Use the disposable black imaging sheets located in the “Kinetic Mats” drawer in SB223, instead of reusable plastic sheet, to be placed inside the imaging chamber for imaging.

- All the animal wastes need to be collected in a trash bag that labeled with date, radioisotope name, and half-life.  The trash bag will be placed behind the lead shielding cabinet in room SB227 after the study for radiation decay.

- After the imaging study, conduct another area survey and record the survey results on the log sheet.  If a small hot spot is detected:

  - Write on the log sheet in detail the location, and Geiger counter reading at 1feet above the surface.

  - Contact the facility staff.

  - Isolate the area by placing a note “Radioactive”, and do not move away any items from the location.

  - Facility staff will clean up the region and assay every single item before removing.  Lead shielding will be applied until fully decayed if RAM cannot be wiped off

- For large spill or radioactive contamination, please call university emergency contact. See below.

- For housing radioactive animals for imaging, please contact Dr. Hong Yuan.  We will coordinate with DLAM for housing.

III. Other Health and Safety Precautions:

- Radionuclide Use - Follow all license conditions as listed in Dr. Hong Yuan’s Radiation Source License # 057-08.

- For any emergency case, please call UNC EHS Radiation safety office at 962-5507 during normal working hours, or 911 after-hours.

- Report all emergencies that threaten life or property to 911.