Exchange Assay (measuring MANT-GTP fluorescence)

2X Exchange buffer

- 40 mM Tris, pH 7.5	(1 mL of 1M)

- 400 mM NaCl	(0.5 mL of 5M)

- 20 mM MgCl2	(0.25 mL of 1M)

- 2 mM DTT		(0.05 mL of 1M)

- 10% glycerol

- H2O to 25 mL

1X Protein Dilution buffer

- 20 mM Tris, pH 7.5 	(0.5 mL of 1M)

- 200 mM NaCl 		(0.25 mL of 5M)

- 1 mM DTT		(0.025 mL of 1M)

- 10% glycerol

- H2O to 25 mL

Also needed:

- 10 μM mant-GTP (4 μL in 2 mL H2O)

- 20 μM stocks of all GEFs (use protein dilution buffer)

- 100 μM stocks of all small G-proteins (preferable…if not enough small G-protein is available, use highest possible concentration to adjust final concentration in cuvette to 2 μM (use protein dilution buffer)

Experimental procedure

|  | (+) control | (-) control | with GEF | Cf |
| --- | --- | --- | --- | --- |
| 2x Exchange buffer | 500 | 500 | 500 |  |
| water | 430 | 440 | 430 |  |
| 10 μM mant-GTP | 40 | 40 | 40 | 0.4 μM |
| 100 μM small G-protein | 20 | 20 | 20 | 2 μM |
| 20 μM GEF/ EDTA | 10 EDTA | 0 | 10 GEF | 0.2 μM |

- all volumes are in μL

- place cuvettes in fluorimeter so that the numbers on the cuvette are facing away from the arrow

- add buffer, water, GTP, and G-protein to the cuvette in the order listed and allow solution and fluorescence reading to equilibrate for 200 seconds.

- Add GEF or EDTA to cuvettes and close cover to fluorimeter.

- Let reactions run until curves are asymptotic

- Waterbath temp set to 20ºC unless otherwise indicated

*The EDTA control is used to verify that the G-protein is active

*If the volume of the G-protein must be adjusted to adjust the concentration, compensate adjusting the volume of water so that final volume equals 1 mL.