## Slide 1: Diffusion MRI - Lesson 4 Atlases, Fibers and Profiles
Martin Styner UNC
Thanks to Guido Gerig, NYU
And many, many folks

## Slide 2: Content
The UNC-NAMIC Atlas Fiber Analysis (done)
Unbiased DTI atlas building via DTIAtlasBuilder (done)
Tracking fibers via AutoTract
  Editing tracts in Slicer and FiberViewerLight
Extracting fiber profiles via DTIAtlasFiberAnalyzer
Statistical Analysis via FADTTSter

## Slide 3: UNC-NAMIC DTI Fiber Analysis - AutoTract
DTIPrep/Topup/Eddy
DTIAtlasBuilder
AutoTract/Slicer/FiberViewerLight
DTIAtlasFiberAnalyzer
FADTTSter/Slicer

## Slide 4: Automated Fiber Tractography
Manual fiber tracking is highly variable and time consuming (~ weeks for brain)
  Seed region specification
  Clean up
  Consistency in definition
Fully automated
  Error prone due to large variability across subjects

## Slide 5: Semi-Automated Fiber Tractography
Try fully automated
  Add manual intervention to correct
Here:
  AutoTract for automated tractography
  3D Slicer for removing tract parts that reach incorrect locations
  FiberViewerLight to remove small fibers and fibers the fold over

## Slide 6: AutoTract Pipeline
Registration of Atlas with Known Tracts
Seed Regions from Propagated Tracts
Tractography from Seed Regions
Fiber Filtering via
TRAFIC
Notes: Make inputs/outputs explicit
Voxel + dilation

## Slide 7: AutoTract GUI
AutoTract (v 4.0)
Set your DTI input data
  Optional data is rarely needed
Set Output dir

## Slide 8: Atlas Registration
Prior atlas/template with
  DTI Image (as NRRD) on first tab
  Known fiber tracts (as VTK files)
Registration with DTI-Reg
  Same as DTIAtlasBuilder
  Same settings
Output
  Registered DTI
  Propagated data
    Tracts: *_t.vtk
Notes: The transformations generated during this process are concatenated and a global displacement field is generated for each subject. Each subject is transformed into the atlas space. However, to re-sample the tensors, Riemannian methods are used to preserve their shape and orientation. The transformed images are averaged using the Log-Euclidean method to produce a tensor atlas. The tensor atlas provides an image with improved signal-to-noise ratio (SNR) that is used to create template fiber tracts. These template bundles are traced and validated by experts. In the following section, the traced fiber bundles will be used to train the neural network.

## Slide 9: Tractography
Voxelized propagated tracts => see regions
  Dilation for optimistic regions
Slicer based seed region tractography (forward propagation with 2nd order Runge Kutta)
  Same parameters as interactive tractography
Result: optimistic tracts
  Fibers of interest in tract
  But also much more…
Notes: 2. Tractography was performed by following small steps along the principal diffusion direction
3.
Concise s
Standart deterministc tract

## Slide 10: Automatic Cleanup: TRAFIC
TRAFIC: TRAct Fiber Classification
Deep neural network to label fibers
  Needs to be trained:
    Currently: 1-2y EBDS atlas, primate atlas
  Best run on a GPU node/station
  Features: curvature & distances to atlas landmarks

## Slide 11: Structure of interest - Arcuate Fasciculus
b) Arcuate Fronto Parietal
d) Arcuate Fronto Temporal
c) Arcuate Temporo Parietal
a) Whole Arcuate Fasciculus
Notes: The Arcuate Fasciculus Right Frontotemporal (ArcRFT) shown in Figure 5, was chosen to test our method because it is a bundle that is difficult to trace, is not always present, or it may be a short bundle.
The role of this fiber bundle is still uncertain and current evidence suggests that it has an important role in language development.
We used 8 different brain atlases of neonate infants of 1-2 years old to build our data set.
50 subjects for classification.

## Slide 12: Training features - Landmarks clustering
5 landmarks per tract
53 bundles, i.e., 265 landmarks
  Clustering using affinity propagation.
  Final number of LM: 32
Notes: In a multi-class classification scenario, we aim to create 53 different classes. Since the number of classes is 53, this will increase the number of features to 268 and rend the neural network training impractical. To reduce the number of landmarks, we applied affinity propagation, which is a type of clustering algorithm that finds N “exemplars points” representative of a cluster given the number N. Figure 2 shows the number of landmarks kept after the affinity propagation algorithm was applied to the set of 265 landmarks (5 for each bundle) which is set to N = 32.

## Slide 13: Neural Network Design
Batch normalization
4 Hidden layers
  1024 hidden units
  Rectified linear units
Score layer
  Softmax with 53 outputs
Adam optimizer
  Learning rate 1-4
Number of epochs 10

## Slide 14: Training features – Distance to landmarks
Video missing due to size restriction

## Slide 15: Clean up
Load automatic fiber into Slicer
Use Fiber Bundle Display to remove unwanted fibers via ROI Selection (video)
Use FiberViewerLight to remove fibers that are too short or too long

## Slide 16: Fiber clean up – Arcuate Fasciculus Left Fronto Temporal – no TRAFIC
Video missing due to size restriction
Notes: The WM region can be provided as input to Autotract or it is calculated using the FA map and thresholding with Otsu’smethod.
The CSF mask can also be provided as input or it is generated with a multi Otsu threshold segmentation.
Specifically, the FA is divided into three clusters and the CSF is considered to lie in the first cluster.
The fibers are pruned according to following criteria:
Source => Fiber atlas,
User provide CSF and WM is best -> Automatic mask creation for CSF and WM

## Slide 17: FiberViewerLight
Allows clustering based cleanup
Main use: length cleaning
  Select VTK Input
  Output Folder
    Distance matrixes
    Temp result
  Classic: Compute exact distances
  Danielson: Approximate via distance transform

## Slide 18: Length based Clustering
Fiber min/max are used as default values
Bars option is the number of bars that will be used on the histogram
Click on Apply Threshold to display the filtered fiber bundle
Click Next or Undo to go back to the main screen
Next will keep changes
Don’t forget to save!

## Slide 19: Length Method
Colors go from blue (shortest) to red (longest)
Adapt thresholds to remove too long or too short fibers
We should put this in 3D Slicer!
(we actually did, but I can’t find the module)

## Slide 20: UNC-NAMIC DTI Fiber Analysis - DTIAtlasFiberAnalyzer
DTIPrep/Topup/Eddy
DTIAtlasBuilder
AutoTract/Slicer/FiberViewerLight
DTIAtlasFiberAnalyzer
FADTTSter/Slicer

## Slide 21: Fiber based Analysis
Analyze corresponding fiber locations across datasets via atlas
  Mapping into atlas
  Inverse map to sample fibers
  Compute fiber profiles
    FA, MD, AD, RD…
  Analyze the profiles
Atlas Fiber

## Slide 22: DTI Property Fiber Profiles
Profile = Distribution of DTI values across fiber bundle
  Average & deviation
Parameterization of each fiber along fiber bundle
  Uniform stepsize
  Origin definition
    Manual (FVL) or Automatic (x2)
Profile extracted via Gaussian Kernels
0
+L
-L

## Slide 23: DTI Atlas Fiber Analyzer
Separate tool called from Slicer
  Diffusion
  FiberAnalysis
  DTI Atlas Fiber Analyzer
Command line call

## Slide 24: DTI Atlas Fiber Analyzer
Made for analyzing many datasets at once
.csv = comma separated value
Data can be prepared with Excel or other editors
Data from DTIAtlasBuilder can be directly loaded
Tabs for the 3 main steps
Load prior csv file
DataTable Area

## Slide 25: Data Definition
Double click headers to edit
Set ID column
Set orig DTI column
Set warp colum
Double click on “no data” to browse for datafile
Double click on “no deformation” to browse for deformation file

## Slide 26: Save the CSV Data
Save CSF File (if necessary
Set Output folder for processing data
Next Step

## Slide 27: Step 2: Atlas Definition
Set Atlas to fiber atlas
  Available fibers are automatically detected
Select fibers to be analyzed
  Add Genu or Add All
“Apply” to run. If data already exists, it will ask about rerun
“Next”

## Slide 28: Step 3: Fiber Profiles
Manual vs Auto origin
  Use Auto with Median
Select Properties
Adapt Fiber tract sampling
  if needed. 1.0 is fine for human data
“Apply” to run & wait, then “Next”
  This can take long

## Slide 29: Output Organization
Parameters
Per Case Data
  Fiber with DTI data
  Profiles
Combined Profiles
  Per tract
Atlas Fiber Data
  Fiber params
    Arclength info

## Slide 30: Stats in Summary CSV
Fiber profiles are all gathered in single CSV
Use Excel for plotting
Use your favorite stats tool for analysis
  FADDTSter
Average FA per tract is easy to compute
You can merge results back with parametrized fiber
  Last Step: MergeStatWithFiber

## Slide 31: Visualization in Slicer
Load parameterized genu fiber
  Add Data => ProfileOutput/Fibers/Genu_parametrized.vtk => as Model
Enable scalars and use FiberLocationIndex

## Slide 32: Alternative Visualization
ShapePopulationViewer
  Allows you to see multiple fibers & cases at the same time

## Slide 33: Example Visualization
Anesthesia effect in macaques

## Slide 34: Conclusions
Define fibers in atlas space with AutoTract
Extract profiles with DTIAtlasFiberAnalyzer
Next: analyze the data! FADTTSter

## Slide 35: FADTTSter
FADTTS = Functional Analysis of Diffusion Tensor Tract Statistics
  Method by Hongtu Zhu for the functional analysis of diffusion profiles
  Cross-sectional analysis
  Omnibus (combined FA, MD, RD, AD) and posthoc tests
FADTTSter: GUI tool by J Noel
  - Input: DTIAtlasFiberAnalyzer files + Demographics/Covariate file

## Slide 36: FADTTSter: Input

## Slide 37: Data Matchup
Matching profiles to subject info

## Slide 38: Profile QC
Cropping profiles
Removing profiles with low correlation to average profile

## Slide 39: Execution
Specify FADDTS location, #perms, output location
Computation time significant

## Slide 40: Plotting Results: Raw Data
Raw data profiles & mean profiles

## Slide 41: Plotting Results: Betas
Betas from GLM – by diffusion property or by covariate

## Slide 42: Significance Plots
Beta & P-values combined